## Slide 1: Predicting Failure for an Open-Hole Multilateral Well
Courtesy of:
  Roberto Suarez-Rivera rsuarez@terratek.com
  TerraTek Salt Lake City (Utah) www.terratek.com

## Slide 2: Introduction
Emplacing arbitrary well geometries, including horizontal and branching segments enhances oil recovery but can be very expensive.
Some configurations are unstable and can lead to mechanical failure if the hole is left open or uncased.
This model evaluates if pumping from an open-hole multilateral well will cause it to fail.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3: Example
Inspired by Roberto Suarez-Rivera of TerraTek (Salt Lake City, Utah) Material properties and well geometry come from the Terratek database (Ebase).
Flow is one-way coupled to structural deformation for the simulation, failure criteria are automatically calculated from results.
Features in COMSOL Multiphysics
  Darcy’s law for flow – Earth Science Module
  3D Solid for structural deformation – COMSOL Multiphysics core package
  Alternatively, one can use elasto-plastic deformation options available in the specialized Structure Mechanics Module
  Failure criterion evaluated by adding user-defined expressions to model
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: Model Geometry
Junction is section of a long well
Horizontal orientation, well diameter is 8.5 inch
Domain is lower half of 80 x 80 x 80 inch box
Originally there is no flow - pumping sucks fluid from reservoir into the well
The pressure drop stresses the reservoir and deforms it.
Is it enough to collapse the well?

## Slide 5: Equations
Structural deformation
Fluid flow – Darcy’s law:
p = pressure
 = permeability
 = dynamic viscosity
grad p gives
directional loading
u = displacements (vector)
 = strains (tensor)
= stresses (tensor)
F = forces or loads (vector)
D = tensor involving
E (Young’s modulus)
 (Poisson’s ratio)

## Slide 6: Boundary conditions
p = po
u,v,w = 0
normal flow=0
v = 0
normal flow = 0
v = 0
p = po
u,v,w = 0
p = po
u,v,w = 0
p = pw
F = known
back
side
front
base
side
top
well
normal flow = 0
w = 0

## Slide 7: Mesh parameters
We choosen to have COMSOL Multiphysics
automatically mesh the geometry
with globally coarse discretization
COMSOL Multiphysics automatically zooms in on nuances in the geometry

## Slide 8: Results - Flow
Fluid pressure – isosurfaces
Fluid velocity - streamlines
Pressure decreases from reservoir to well bore
Minute pressure change inside split
Flow speeds up en route to wellbore, except velocity is low inside split (note streamline color)

## Slide 9: Results
Displacement – surface
Displacement - deformation
Displacements from pumping decrease size of borehole opening
Little displacement inside split
Greatest impact “above” split

## Slide 10: Results – Flow and Displacement
pressure – isosurface, velocity – stream tubes, displacement – mesh and deformation

## Slide 11: Results – Failure Criterion
For this well and pumping rates:
failure could start here but unlikely
mostly safe throughout

## Slide 12: Points of interest
Geometry, data, and general approach from Roberto Suarez-Rivera at TerraTek (www.terratek.com). Approach hinges on calibration to data. Useful here was extensive data library from Ebase of Terratek (www.terratek.com).
Multiphysics combination of predefined equations: Darcy’s law (Earth Science Module), 3D solid (COMSOL Multiphysics).
Unusual capability to arbitrarily define link between flow and structure equations.
Failure equation as user-defined post-processing option on elastic deformations obtained with COMSOL Multiphysics core package; elasto-plastic behavior possible with Structural Mechanics Module.

## Slide 13: References
[1] Suarez-Rivera, R., Begnaud, B.J., and Martin, W.J. 2004. Numerical analysis of open-hole multilateral completions minimizes the risk of costly junction failures. Rio Oil & Gas Expo and Conference 2004 Proeceedings. Instituto Brasileiro de Petróleo e Gás, IBP096_04.