## Slide 1: COMSOL Multiphysics Non Destructive Testing

## Slide 2: Model Specifications
Elastic waves are produced from stresses exerted by small elements embedded in the metal plate
Metal plate dimensions: 150mm x 80mm x 7.5mm
Cylindrical fault modeled in the metal plate
Out of phase stresses applied on four embedded elements, considered only on the surface
Presentation layout
  Geometry
  Meshing
  Physical properties and boundary conditions
  Postprocessing

## Slide 3
Model Description
Begin by selecting a 2d geometry without choosing any physics

## Slide 4: Geometry
2d geometry drawn
using the line tool
Metal plate
Embedded elements
Fault
PML
PML
PML
PML
Now, go to
Draw -> Extrude and
extrude 2d geometry
in the z-direction

## Slide 5
Note that the element ‘slabs’ run through the plate thickness to ensure a uniform mesh.
Physically, the elements are
relevant only on the surface, as can be seen later in the presentation
Geometry

## Slide 6: Geometry and Meshing
Free mesh used on top surface
Go to Mesh -> Free Mesh Parameters, enter required (problem specific) parameters and press ‘OK’

## Slide 7
Meshing
Swept mesh used in the z-direction to ensure sufficient meshing in z direction
unstructured mesh on surface
Structured mesh in z-direction

## Slide 8
Go to Multiphysics -> Model Navigator
and add the required physics in the 3d geometry
Physical properties

## Slide 9
Physical properties
Material properties defined under ‘Material’ tab
Perfectly matched layers used on all plate edges to model infinite domains

## Slide 10
Boundary Settings
Edges of PMLs are fixed boundaries
All other boundaries are free to move
Loads applied on the elements on the upper surface (see next slide)

## Slide 11
Boundary Settings
Out of phase loads applied to the four elements on the surface

## Slide 12
Boundary Settings
Note that interior boundaries of the slabs are deselected, implying they are part of the metal plate itself.
Physically, this implies that the elements are considered only on the surface.
Ie. the interior boundaries only affect the mesh, not the physics
Model solved using default settings, over a frequency range of 50 kHz to 0.1 MHz

## Slide 13
Postprocessing
Choose quantities to plot from predefined list or enter any desitred expression
Plot shows total deformation (on an exaggerated scale)

## Slide 14
x-displacement
z-displacement
Postprocessing

## Slide 15
Postprocessing
Particle displacement plot per requirements (thickness on y axis)

## Slide 16: Contact Information
Mia Johansson
miaj@comsol.com
Vineet Dravid
vineet@comsol.com
COMSOL, Inc.
781-273-3322
Support e-mail: support@comsol.com
Telephone support via local office:
  Burlington, MA, 781-273-3322
Notes: <number>
<footer>
<header>
<date/time>
Web-Based Training
Train at work or at home
Connect at your convenience
On-Site Training
Bring training to your site
Custom courses available